## Slide 1: Upgrade Firmware Ruijie RSR10-01G-T(W) to English
February 2018

## Slide 2: Login to WEB GUI
Configure PC using 192.168.1.xxx/24 IP
Plug LAN cable PC to port1 Router
  Ping to verify
Open http://192.168.1.1 on browser and login using username/password : admin/admin

## Slide 3: Download Firmware from website
Open this Link :
https://ruijienetworks.com/support/software-downloads/cp_rsr-10-01g-tw-series-routers

## Slide 4: Extract firmware file

## Slide 5: Upgrade firmware to English Ver.

## Slide 6: Upgrade firmware to English Ver.
Choose firmware that we have downloaded before

## Slide 7: Upgrading process
Waiting until upgrade process bar to 100% then router will reboot
It say , upgrade already finished

## Slide 8: Clear Browser Data (cache)
On browser, push CTRL + H to open history menu
Choose clear browsing data
Choose delete 1 hour data

## Slide 9: Login again

## Slide 10: GUI already in English

## Slide 11: Documentation File
Datasheet https://ruijienetworks.com/resources/preview/41510
Installation Guide https://ruijienetworks.com/resources/preview/41510
Configuration Guide https://ruijienetworks.com/resources/preview/57877